Elton Cheng
ME333
Final Project
3/12/2017
28.4.1
1. SPI Channel 4. Uses pins F4, F5, B14 and B8
2. I used pin B0 as ADC input AD1.
3. I will be using the motor, current sensor, and battery. Pin D0 will be responsible for sending the PWM signal, and D3 will be a digital output pin to control direction.
4. Use Timer3 for the 5kHz ISR and Timer4 for the 1kHz ISR. Current control will have a higher priority over position control, so current control will be at priority 5, and position at 4.
5.
Trajectory Generator:
Reference Position:
Motion Controller:
Torque/Current Command:
Current Controller:
PWM Duty:
H-Bridge:
Actual Current:
Current Sensor:
Measure Current:
Motor:
Motor Position:
Encoder/Tachometer:
Measured Position/Velocity:

6. See attached drawing.

28.4.7
2. 6.4 V on battery voltage. 16 R of the motor. Therefore, Imax = .8 A
3. .012 V
4. R2/R1 = 137; Chose 100 kOhm and 1kOhm to get 100 gain
5. 10 kOhm Resistor and 10 nF Capacitor
6.
R0	Expected I (mA)	Measured I (mA)	Sensor (V)	ADC (counts)
10 (to RS+)	600	347.4	2.18	681
20 (to RS+)	300	221.5	1.96	616
40 (to RS+)	150	127.7	1.81	565
Open Circuit	0	.14	1.61	503
40 (to RS-)	-150	125.9	1.40	434
20 (to RS-)	-300	218.9	1.25	393
10 (to RS-)	-600	341.3	1.05	331

28.4.9
See attached drawing.

28.4.10
Attach plot of ITEST. Kp = .35, Ki = .1

HOLD. Kp = .4, Ki = 0, Kd = 10

28.4.12
Attach plot of TRACK